## Slide 1
Autonomous Hemispherical Spatial Mapping & Target Detection
A Robust Time-of-Flight (ToF) Approach for Static Target Localization
Team RoboWizards
R Sabarish Mandar Patil Rijul MK

## Slide 2
Problem Understanding: The Challenge Ahead
Stationary 2-DoF Scanning System
Design a fixed system capable of precise spatial analysis.
Hemispherical Mapping
Map the upper hemisphere of a closed enclosure with accuracy.
Autonomous Target Detection
Reliably detect and count static targets without human intervention.
ToF Sensing Constraint
Exclusively utilize Time-of-Flight technology.
No Double-Counting
Implement robust algorithms to prevent redundant target identification.
Cuboidal Enclosure
Adapt to varying wall distances within a constrained environment.

## Slide 3
System Architecture: A Synergy of Components
The Master: Laptop (Windows)
Responsible for processing: mapping, filtering, and 3D visualization.
The Slave: Arduino Nano
The embedded control unit, driving motors and precisely triggering sensor readings.
The Sensor: VL53L0X ToF
Provides precision distance measurements with millimeter accuracy, forming the backbone of our spatial data.
The Mechanism: 2-DoF Pan-Tilt Servo Turret
Enables comprehensive hemispherical scanning with Azimuth: 0°-180° and Elevation: 0°-180° for full front and back coverage.

## Slide 4
Methodology: The Power of ToF
Pivot from Vision to Active Sensing
ToF is Lighting Independent: Our Time-of-Flight sensor operates flawlessly in complete darkness or bright ambient light, ensuring consistent performance.
Direct Depth Data: Eliminates the need for complex stereo-vision computations, providing immediate physical coordinates for objects in space.
Efficient Scanning Strategy
Zig-Zag Raster Scan: An optimized path planning approach (Left→→Left) ensures efficient data acquisition across the scanning area.
Full Coverage with 180° Tilt: By utilizing the full 0-180° tilt range, the system scans both the front and back hemispheres, achieving comprehensive coverage without a 360° motor. Imagine the camera looking forward (0-90) and then doing a "backflip" (90-180) to scan behind.

## Slide 5
Algorithm Phase 1: Robust Mapping with Background Subtraction
Addressing the "Cuboid" Problem.
01
The Challenge: Simple Thresholding Fails
Traditional depth thresholding proves inadequate as cuboid corners are inherently farther than wall centers, leading to inaccurate target identification.
02
Step 1: Calibration - Baseline Depth Map
An initial scan of the empty room creates a comprehensive baseline depth map, establishing the reference environment.
03
Step 2: Differential Analysis
By comparing real-time scans against the baseline, we isolate new objects by identifying significant depth deviations.
04
Result: Ignored Geometry, Highlighted Targets
The system effectively filters out the room's geometry, focusing solely on "new" mass, thus highlighting potential targets with high precision.

## Slide 6
Algorithm Phase 2: Signal Processing for Clarity
Noise Reduction
Multi-Sampling: The Arduino acquires three readings per data point and averages them, effectively mitigating sensor jitter and improving data accuracy.

## Slide 7
Algorithm Phase 3: Clustering & Counting for Precision
Masking
Generates a binary map, precisely outlining all valid target points within the scanned environment.
Morphological Closing
Effectively "glues" fragmented nearby points, filling any gaps where the laser might have missed, ensuring complete object representation.
Contour Detection
Identifies and counts distinct "blobs" in the 2D map, representing individual target objects and preventing overcounting.
Centroid Calculation
Computes the mathematical 3D center of each target's point cloud, providing precise localization by calculating its centroid.

## Slide 8
3D Visualization: Real-time Spatial Awareness
Key Features of the 3D Map:
Gray Points: Represent the reconstructed enclosure, providing spatial context derived from calibration data.
Red Points: Highlight the detected target clusters, showing the presence and shape of identified objects.
Black Stars: Mark the computed centroids of the targets, indicating the precise mathematical center of each object.
Outcome: A fully interactive 3D Spatial Map, generated.

## Slide 9
Challenges & Robust Solutions
Sensor Noise
Implemented Multi-sampling (Arduino) & Median Blurring (Python).
Room Geometry
Utilized Background Subtraction instead of fixed thresholds.
Blind Spots
Enabled 180° Tilt for "Over-the-Top" scanning, ensuring full 360° coverage.

## Slide 10
Conclusion: Dimension-Independent Detection
The system successfully maps a 3D environment, intelligently filters out enclosure geometry, and accurately counts static targets regardless of their shape or size.
Key Achievement
Dimension-Independent Detection: Our system adapts to and performs reliably in any room shape, overcoming previous limitations.
Future Scope
Exploring increased scan resolution or implementing a continuous "Lidar-style" spin for significantly faster data acquisition and real-time responsiveness.

## Slide 11
THANK YOU